Car Lift Operation

Only Bloominglabs members may operate the lift. Members must go through the qualification process to get the code to the power lock box. Members may operate the lift on behalf of non-members.

Operating procedure:

1). Sign damage liability waiver if you have not already done so

2). Park car between lift towers

3). Swing yellow lift arms under car so pads will lift against car frame – get help if unsure!!

4). Arms will automatically lock in place upon lifting

5). Remove padlock from lift electrical box, throw lever to ON position

6). Use push-button on the lift motor to raise the vehicle.

Periodic “knocks” from both lift towers are normal and are caused by the safety interlock.

Lowering procedure:

1). Ensure no parts, tools, or people are under the vehicle

2). Pull the safety release cables hanging from each lift arm (2 cables total)

Cables do not need to be held while lift is lowered

3). Push hydraulic release lever to lower vehicle

4). Swing yellow swing arms out from under vehicle

5). Back vehicle out of workshop, relock garage door

6). Turn off lift power, relock lift power box

Car Lift Operation

If the lift does not go down:

First verify if you pulled BOTH release cables under the lift. If you did not do this then this is how to recover:

First raise the lift back up a few inches. Now pull BOTH release cables. The cables to not need to be held during operation. Now push the down lever, the lift should come down properly.

UP

Power is locked out 
at breaker panel

DOWN

Pull BOTH release cables first

Re-lock electric box when done

Lift Power

ONLY MEMBERS MAY OPERATE LIFT

You must be qualified on operation

before getting the lock code

RELOCK WHEN DONE